## Slide 2
The Intervals pane sets the total duration of the simulation.
Ambient fluid will flow into the domain’s left inlet
Simulation lasts 20 years

## Slide 3
Add any injection fluids on the Fluids pane.
Contaminated water
Click to add a new fluid
Clean water

## Slide 4
Click to expand view
Use the Wells pane to set the name, location, chemistry(s), and flow rate(s) of wells.
Click to create a new well

## Slide 5
Well “leak_1” injects contaminated fluid for first 10 years
XY position
Positive rate indicates injection
Injection fluid

## Slide 6
Well “extract” produces water after 10 years
Negative rate indicates withdrawal (no need to specify injection fluid)

## Slide 7
Pb++ contaminated water enters the domain through three point sources (injection wells).
Contour lines represent hydraulic potential.

## Slide 8
Production well draws contaminated fluid out of the aquifer.

## Slide 9
For the “recirculator” well, reinject whatever comes out of the “extract” well
As an alternative to setting injection fluid chemistry, you can recirculate the fluid produced from any extraction well.

## Slide 10
Click to add new well intervals
For each well, you can add any number of “well intervals”
Inject different fluids, change pumping rate, or turn well on or off over time